## Slide 1
Nanotechnology and the Environment
Dr. Maidul Hossain
Nano Grantees’ Progress Review Workshop Philadelphia, PA

## Slide 2: What is nanotechnology? What is Different/Special about nano? What is the scope of nanotech now that might impact the environment? The relation of environmental protection to nanotechnology Research Framework Research-related issues-reports Current EPA activities What we hope to get from sponsored academic research
Outline

## Slide 3
While many definitions for nanotechnology exist, the NNI* calls it "nanotechnology" only if it involves all of the following:
1. Research and technology development at the atomic, molecular or macromolecular levels, in the length scale of approximately 1 - 100 nanometer range.
2. Creating and using structures, devices and systems that have novel properties and functions because of their small and/or intermediate size.
3. Ability to control or manipulate on the atomic scale.
What is nanotechnology?
*National Nanotechnology Initiative

## Slide 4
100 µm
10 µm
1 µm
100 nm
10 nm
1 nm
0.1 nm
Conventional
Filtration
Microfiltration
Ultrafiltration
Reverse
Osmosis
H
2
O
(0.2 nm)
Hemoglobin
(7 nm)
Virus
(10-100 nm)
Microbial
Cells
(~1 µm)
Protozoa
(>2 µm)
PM 2.5
Aerosols
Nanoscale contaminants in
water and air (little is known)
Size Spectrum of Environmental Particles
Pollens
(10-100 µm)
Adenovirus 75 nm
Bacteriophage 80 nm
Influenza 100 nm
E. Coli
1000 nm
Fullerenes, nanotubes
After Wiesner

## Slide 5
Nanostructure
Size
Example Material or Application
Clusters, nanocrystals, quantum dots
Radius:
1-10 nm
Insulators, semiconductors, metals, magnetic materials
Other nanoparticles
Radius:
1-100 nm
Ceramic oxides, Buckyballs
Nanowires
Diameter: 1-100 nm
Metals, semiconductors, oxides, sulfides, nitrides
Nanotubes
Diameter: 1-100 nm
Carbon, including fullerenes, layered chalcogenides
Adapted from J.Jortner and C.N.R.Rao, Pure Appl Chem 74(9), 1491-1506, 2002
What are the materials of nanotech?

## Slide 6
How can these properties be used to protect the environment?
Nanomaterials have unique properties
VDI

## Slide 7
Characterizing Nanomaterials

## Slide 8
Applications of Nanotechnology
VDI

## Slide 9
Applications of Nanotechnology
VDI

## Slide 10
We are at the beginning of a Revolution in:
How things are made
And whether they are made
Where things are made
Rejeski, 2003

## Slide 11
Rip van Winkle Scenario
Slow Learning/Adaptation
Environmental impacts are an unintended consequence
of technology development and deployment
and
Regulation must be applied to reduce impacts
Two Scenarios for coping with the new revolution
Vulcan Scenario
Fast Learning/Shaping
Environment is co-optimized as a part of technology development
and deployment, or is the primary goal
Rejeski, 2003

## Slide 12
The Challenge
Use nanotechnology research to:
…Help clean up past environmental damage
…Correct present environmental problems
…Prevent future environmental impacts
…Help sustain the planet for future generations

## Slide 13
Implications of
interactions of nanomaterials with the environment and
possible risks that may be posed by the use of nanotechnology.
A Research Framework for Nano and the Environment
Applications
reactive to existing problems
or
proactive in preventing future problems.

## Slide 14
Applications-Sensors
improved monitoring and detection capabilities, better controls
real-time, accurate sensing of many compounds simultaneously at extremely low concentrations frequently in hostile environments
Applications-Treatment
Applications-Remediation
Cleaning up waste streams of contaminants, particularly those substances that are highly toxic, persistent within the environment, or difficult to treat
promise for cost-effective, specific, and rapid solutions for treatment of contaminants
Cleanup of contaminated sites with problems brought about by prior technologies and past practices.
Information for Environmental Protection/Risk Management--More efficient use of materials, more data on wastes
Notes: Nanotechnology shows great promise for improved sensors. The sensors can lead to improved monitoring and detection capabilities that allow for real-time, accurate sensing of many compounds simultaneously at extremely low concentrations frequently in hostile environments[BK1].
Treatment involves cleaning up waste streams of contaminants, particularly those substances that are highly toxic, persistent within the environment, or difficult to treat. Nanotechnology holds promise for cost-effective, specific, and rapid solutions for treatment of contaminants[BK2].
Remediation addresses problems brought about by prior technologies and past practices. Cleanup of contaminated sites using nanotechnology is one of the initial successes in nano tech applications to the environment. Researchers are developing cost-effective technologies that enable both rapid and effective cleanup of recalcitrant compounds, particularly those located in inaccessible areas[BK3].
There are two aspects of nanotechnology applications in green manufacturing. The first involves using nanotechnology itself to eliminate the generation of waste products and streams by designing in pollution prevention at the source. The second aspect involves the manufacture of nano materials themselves in a benign manner. Both of these involve use of environmentally friendly starting materials and solvents, improved catalysts, and significantly reduced consumption of energy in the manufacturing process[BK4].
Nanotechnology can help the environment through enabling green energy. Nano products such as Solar and fuel cells could lead to commercially viable alternative clean energy sources[BK5].
[BK1] Use Tao, Wan Shih, Gawley, Trogler
[BK2]point and shoot, membranes
[BK3]Zhang, Bhattycharia, other zero valent iron
[BK4]filters, separations, molecular manufacturing
[BK5]check 03 symposium for examples

## Slide 15
Applications-Green Manufacturing
two aspects:
--using nanotechnology itself to eliminate the generation of waste products and streams by designing in pollution prevention at the source.
--manufacturing nanomaterials themselves in a benign manner.
Both aspects involve use of environmentally friendly starting materials and solvents, improved catalysts, and significantly reduced energy consumption in the manufacturing process
Applications-Green Energy
Nano products such as Solar and fuel cells could lead to commercially viable alternative clean energy sources
Atom-by-atom construction--Less material to dispose of
Dematerialization- less “stuff” to begin with
Energy savings via light weight composites, embedded systems

## Slide 16
Implications-Nano-Geochemistry
Implications-Toxicity
Knowledge of formation of atmospheric aerosols, and the movement of natural nano particles in air and soil can help inform the solutions to man-made problems
Implications-Fate, Transport, Transformation
Implications-Exposure, Bioavailability, Bioaccumulation
Implications-Industrial Ecology Aspects
Determine exposure routes for both natural organisms in a variety of ecosystems and for humans in the environment[
Essential to risk analysis for ecosystem and human health
Also essential to risk analysis
Determine where in its lifecycle a nano material may cause impact to the environment, examine materials flow changes and environmental effects; use DfE, MFA, LCA tools
Notes: Many natural processes on the nanoscale have implications in the environment. Studies of nano geochemistry, the formation of atmospheric aerosols, and the movement of natural nano particles in air and soil can help inform the solutions to man-made problems[BK1].
The implications of fate, transport, and transformation of manufactured nano materials in the environment will determine exposure routes for both natural organisms in a variety of ecosystems and for humans in the environment[BK2].
Nanotechnology has many implications for the environmental health of human beings. The implications become part of the information necessary to analyze risks of new materials and products. A major part of risk analysis is determining whether there are any harmful effects to health from the materials or products under consideration. Determining whether or not nano materials are toxic is of major importance in basic risk analysis. The other aspect of risk analysis involves exposure and bioavailability[BK3].
Industrial ecology, in particular, materials flow analysis and lifecycle assessment are useful to determine where in its lifecycle I nano material may cause impact in the environment. Lifecycle analysis can help determine whether the environment will be affected during the extraction of the material, during production, during product use, or at an end of life. Materials flow analysis, especially when used in a comparative manner for new technologies, offers a side-by-side comparison of current technologies with new nanotechnologies[BK4].
[BK1]ultrafines froins , etc.
[BK2]Wiesner, particulates in environment
[BK3]Lam, Warheit, Oberdorster
[BK4] Lloyd/Lave, Beaver

## Slide 17
Nanostructured Material by Design
Manufacturing at the Nanoscale
Chemical-Biological-Radiological-Explosive
Detection and Protection
Nanoscale Instrumentation and Metrology
Nano-Electronics, -Photonics and –Magnetics
Healthcare, Therapeutics, and Diagnostics
Efficient Energy Conversion and Storage
Microcraft and Robotics
Nanoscale Processes for Environmental Improvement
9 NNI Grand Challenges for Research in Nanotechnology

## Slide 18
1. Applications for Measurement in the Environment
Vision: The unique properties of nanoscale materials will enable the development of a new generation of environmental sensing systems. In addition, measurement science and technology will enable the development of a comprehensive understanding of the interaction and fate of natural and anthropogenic nanoscale and nanostructured materials in the environment.
GRAND CHALLENGE –Environment
2.Applications for Sustainable Materials and Resources
Vision: A society that uses nanotechnology to transform the way it extracts, develops, uses and dissipates materials and the flow, recovery, and recycling of valuable resources, especially in the use of energy, transportation of people and goods, availability of clean water, and supply of food.
Notes: Research needs identified in:
Biological sensor technologies that are sufficiently stable to allow usage on an in-situ, continuous basis for high-density usage
· A general “array” for detection of a wide variety of potential analytes.
· Information concerning the diversity of chemical composition at the nanoparticle level, and the transformations that occur and measurement techniques that distinguish the chemical composition of particle surface layers from the particle interior.
· Generic nanoscale assembly methods.
· Advances in spectroscopic instrument technologies that allow detection of enough signal strength rapidly, while probing smaller volumes of the nano- particulate sample
----
Global Sustainable Energy Systems enabled by photovoltaics and photo-biofuel cells
Optimization of the translocation of people and goods utilizing green vehicles and smart infrastructure
Global sustainable use and quality of water enabled by superior composite and multifunctional materials
Global sustainable agriculture (optimization of production and distribution of food) enabled by development of more effective and less environmentally harmful pesticides and fertilizers.

## Slide 19
Vision: Sustainable manufacturing processes based on the use of nanoscale science and nanotechnology – integrated processes and bottom-up assembly – that can serve human needs and are compatible with the surrounding ecosystems and human population.
3.Applications for Sustainable Processes
Vision: The ability to understand and quantify nanoparticles in Earth system processes in order to anticipate their impacts and thus optimize and integrate environmental sustainability and nanotechnology.
4.Implications in natural and global processes
Notes: Optimizing the use of benign materials particularly through the use of alternative or solvent free processes
Efficient control of manufacturing processes with sensors and actuators
Controlled selectivity and greater efficiency in manufacturing processes using nano-enabled, multifunctional, stable catalysts
Integrating biological processing into nano-driven manufacturing
such as through the utilization of the high enantiomeric selectivity using biological molecules (e.g. enzymes, pharmaceuticals), rational modification of multifunctional materials (e.g. linear polymers with pendant reactivity), and manufacture of self-healing nanostructures (e.g. adhesive which could sense its failure and regenerate).
Understand nanoscale phenomena as they pertain to Earth system processes on local, regional, and global scales over a range of time domains
Understand and quantify the inputs, cycling, and effects of nanoparticles in the environment so as to anticipate the impacts of future particle release
Optimize and integrate environmental sustainability and nanotechnology.

## Slide 20
Vision: Development of nanotechnology responsibly with a full appreciation of its health and environmental impacts.
5.Implications in health and environmental safety
Develop high throughput/multi-analyte toxicological methodologies with focus on mechanism and fundamental science of particle toxicity and access to well-characterized nanomaterials for conducting risk assessment research
Better understand the diversity of anthropogenic nanoparticles through the development of a nanomaterial inventory
Gain information on exposure to nanomaterial resulting from medical, occupational, environmental, and accidental release of nanomaterial with regard to the concentration as well as what form(s) the nanoparticles may assume upon release into the environment
Predict biological properties of nanomaterials through toxicological assessment of nanomaterials that includes relevant and scientifically appropriate acute and chronic toxicokinetics and pharmacokinetic studies
Research challenges and needs include:

## Slide 21
Other Grand Challenges and Related Issues
Metrology
Energy
Nomenclature/Classification
Fundamental to study of nanotechnology
Grand Challenge Workshop
Inseparable from environmental aspects
Initiative in hydrogen economy:
Production, storage, use in fuel cells
Smalley’s Energy Challenge
Grand Challenge Workshop
Necessary for environmental assessment
Colvin/Kulinowski proposal, Vision 20/20,NNI
Notes: Production: catalysts for fossil fuel reforming, solar photoelectrochemistry/photocatalysis, bio/bio-inspired production—capture or mimic biological H2 production, nuclear &solar-thermal energy to split water
Storage: metal hydrides & complex hydrides, novel nanoscale materials
Fuel cells: nano-membranes and separations processes

## Slide 22
WWW.EPA.GOV/NCER Go to Publications/Proceedings

## Slide 23
Swiss Re:Nanotechnology Small Matter,
Many Unknowns (http://www.swissre.com/)
International Dialogue on Responsible Nanotechnology(http://www.nsf.gov/home/crssprgm/nano/dialog.htm)
Societal Implications of Nanotechnology
(http://nano.gov/html/res/home_res.html)
Some Documents to be aware of:
Chemical Industry R&D Roadmap for Nanomaterials
By Design: From Fundamentals to Function
(www.chemicalvision2020.org/pdfs/nano_roadmap.pdf

## Slide 24
“it is important that claims of likely environmental benefits are assessed for the entire lifecycle of a material or product, from its manufacture through its use to its eventual disposal.
We recommend that lifecycle assessments be undertaken for applications of nanotechnologies.”
Royal Society Report
(http://www.nanotec.org.uk/finalReport.htm)
VDI Report:Technological Analysis
Industrial application of nanomaterials - chances and risks
http://imperia5.vdi-online.de/imperia/md/ content/tz/zuknftigetechnologien/11.pdf
Call for open public dialog

## Slide 25
Nanotech is both top down and bottom up—like Nature
A. Uses “natural” ingredients-simple atoms
B. at room temperature,
C. With small machines for assembling,
D. in non-toxic solvents,
E. And the end of life disposal is accounted for
The Cell is a Nano Factory!
Notes: From a single cell, the human body contains about 7.5 trillion cells Fast enzymes, e.g., carbonic anhydrase or ketosteroid isomerase can process about a million molecules/sec

## Slide 26: EPA (NCER) Nanotechnology Activities
2001 RFA
Synthesis and Processing;
Characterization and Manipulation;
Modeling and Simulation;
Device and System Concepts
ACS Symposia-2003,04,05
Gordon Conference- 2006?
Grand Challenges Workshop
Interagency Environmental Conference
Edited journals
Grantees’ workshops
Aug.`02, ‘04
Building a Green Nanotech Community
2002 RFA
Environmentally Benign Manufacturing and Processing;
Remediation/Treatment;
Sensors;
Environmental Implications of Nanotechnology
SBIR Nanomaterials and Clean Technologies
Environmental Applications
Applications and Implications
2003/04 RFAs
Health effects of manufactured nanomaterials
Implications
EPA NanoMeeters
Dec. 2003 Societal Implications II
Wilson Center Meetings

## Slide 27
THE CHARGE!
RESEARCH For ENVIRONMENTALLY
RESPONSIBLE NANOTECHNOLOGY

## Slide 28
Come forth into the light of things, Let nature be your teacher
William Wordsworth
Questions??
Karn.Barbara@epa.gov
202-343-9704
www.epa.gov/ncer