## Slide 1: Basic Concepts of Environmental Impact Analysis (EIA)
by
Dr. Misha Roy,
Assistant Professor, Environmental Science
Directorate of Distance education
Vidyasagar University

## Slide 2: What is EIA
Environmental Impact Assessment is
A formal process for identifying:
  likely effects of activities or projects on the ENVIRONMENT, and on human health and welfare.
  means and measures to mitigate & monitor these impacts
Environment is broadly interpreted: physical, biological, and social components in which man and other Organisms lives
In EIA, the term “impacts” is used instead of “effects of activities.”
What is an impact

## Slide 3: What is an impact?
The impact of an activity is a deviation (a change) from the
baseline situation
that is caused by the activity.
The baseline situation is the existing environmental situation or condition in the absence of the activity.
The baseline situation is a key concept in EIA

## Slide 4: The Environmental Impact Assessment Process
Screening
Scoping
Baseline study
Impact Evaluation
Mitigation Measures
Comparison of alternatives
Documentation
EIA Review and Decision Making
Monitoring and Follow-Up

## Slide 5
Proposal Identification
Screening
EIA Required
No EIA
Scoping
Impact analysis
Mitigation and Impact Management
Public involvement
EIA Report
Decision making
Approved
Not Approved
Implementation and Follow Up
Redesign & Resubmit
EIA Process Flowchart

## Slide 6: The EIA process
Scope
Evaluate baseline situation
Identify & choose alternatives
Identify and characterize potential impacts of proposed activity and each alternative
Develop mitigation and monitoring
Communicate and document
Phase I: Initial inquiries
Phase II: Full EIA study (if needed)
Understand proposed activities
Screen
Conduct preliminary assessment (if needed)

## Slide 7: Screening
It would be time consuming and a waste of resources for all proposed projects and activities to undergo EIA
Not all development projects require an EIA, as some projects may not pose an environmental threat
Screening is the process used to determine whether a proposed project or activity requires an EIA and, if so, what level of environmental review is necessary
Screening Criteria

## Slide 8: Screening Criteria
  Project type, location, size (e.g., capital investment, number of people affected, project capacity, areal extent)
  Receiving environment characteristics
  Strength of community opinion
  Confidence in prediction of impacts

## Slide 9: Screen the activity
Screen each activity
Based on the nature of the activity, what level of environmental analysis is indicated?
screening classifies the activity into a RISK CATEGORY:
VERY LOW RISK
VERY HIGH RISK
MODERATE OR UNKNOWN RISK
EIA process ends
Do full EIA study
Do preliminary assessment
The outcome of the screening process determines the next step in the EIA process

## Slide 10: Scoping
A process of interaction between government agencies and project proponents
Identifies:
  spatial and temporal boundaries for the EIA
  important issues and concern
  information necessary for decision making
  significant effects and factors to be considered

## Slide 11: Importance of Scoping
Serves to facilitate efficient EIA by identifying appropriate areas for consideration (e.g, key issues, concerns, alternatives)
Reduces likelihood of deficiencies in EIA (e.g., ensures that important issues are not overlooked)
Prevents unnecessary expenditures and time delays from oversights or unnecessary areas of study

## Slide 12: EIA Impact Identification Methods
Types | Details
1. Simple checklist | Contain specific lists of parameters affected by the project. No information about cause and effect relationship
2. Matrix | Identifies cause and effect relationships between specific activities and impacts
3. Networks | Establish cause condition-effect relationship
4. Overlays | Completion of information about set of maps of project area on various aspects of environmental characteristics – physical, social, ecological, aesthetic. Geographical information system (GIS)
5. Battele Environmental Evaluation System | Ranking

## Slide 13: Selection of Appropriate Methods
Type and size of proposal
Type of alternatives being assessed
Nature of likely impacts
Experience using EIA methods
Resources available
Nature of public involvement
Procedural/administrative requirements

## Slide 14: Checklists
ADVANTAGES
Simple to understand and use
Good for site selection and priority setting
DISADVANTAGES
Do not distinguish between direct and indirect impacts
Do not link action and impact
Qualitative

## Slide 15: Matrices
ADVANTAGES
Link action to impact
Good method for displaying EIA results
DISADVANTAGES
Difficult to distinguish direct and indirect impacts
Significant potential for double-counting of impacts
Qualitative

## Slide 16: Networks
ADVANTAGES
Link action to impact
Useful in simplified form in checking for second order impacts
Handles direct and indirect impacts
DISADVANTAGES
Can become overly complex if used beyond simplified version
Qualitative

## Slide 17: Overlays
ADVANTAGES
Easy to understand and use
Good display method
Good for site selection setting
DISADVANTAGES
Address only direct impacts
Do not address impact duration or probability

## Slide 18: BEES
ADVANTAGES
Excellent for impact identification and analysis
Good for experimenting
Semi-quantitative to quantitative
DISADVANTAGES
Heavy reliance on knowledge and data
Often complex and expensive

## Slide 19: Impact Significance Determination
Impact
Characteristics
(e.g., spatial extent)
Impact
Importance
(e.g., value)
x
=
Impact
Significance

## Slide 20: Characteristics Affecting Impact Significance
Nature of impact (e.g., positive, negative, synergistic)
Extent and magnitude
Timing (i.e., construction, operation, closure)
Duration (i.e., short, chronic, intermittent)
Reversibility/irreversibility
Likelihood (i.e., probability, uncertainty)

## Slide 21: Mitigation Measures
Although it is about impossible to eliminate the adverse environmental impacts altogether, it is often feasible to reduce its intensity. These measures are known as Mitigation Measures
Such measures may be
Engineering Works
Management Practices
The possible mitigation measures include:
Changing project sites, routes, processes, raw materials, operating methods, disposal routes or locations, timing, or engineering designs.
Introducing pollution controls, waste treatment, monitoring, phased implementation, landscaping, personnel training, special social services or public education.
Offering (as compensation) restoration of damaged resources, money to affected persons, concessions on other issues, or off-site programmes to enhance some other aspect of the environment or quality of life for the community.
Mitigation plan should be supplemented with an environmental management plan (EMP) to guide the proponent towards environmental improvements
The implementation of measures designed to reduce the undesirable effects of a proposed activities on the environment


## Slide 22: Assessment of Alternatives
In this step the Environmental
losses and gains will be combined
with economic costs and benefits
It includes-
A summary of Positive and negative environmental impacts
A summary of costs and benefits
Output- Helps decision makers to choose a course of action


## Slide 23: Documentation
An executive summary of the EIA findings.
A description of the proposed development project.
The major environmental and natural resource issues that needed clarification and elaboration.
The project's impacts on the environment (in comparison with a baseline environment as it would be without the project), and how these impacts were identified and predicted.
A discussion of options for mitigating adverse impacts and shaping the projects to suit its proposed environment, and an analysis of the trade-offs involved in choosing between alternative actions.
An overview of gaps or uncertainties in the information.
A summary of the EIA for the general public.

## Slide 24: Decision Making
The decision making starts when the working
document reaches the decision maker. This
includes a list of project alternatives.
Environmental and economic impacts
and recommendations


## Slide 25
Thank You