## Slide 1: 8085 Microprocessor Architecture & Pin configuration
MCA 1ST YEAR 2ND SEMESTER 2020
Paper: MCA 203
Dr. Utpal Nandi
Dept. of Computer Science
VIDYASAGAR UNIVERSITY

## Slide 2: 8085 Microprocessor Architecture & Pin configuration
Pin configuration of 8085
Limitations of 8085
Internal Architecture of 8085
8085 Single board Microcomputer System

## Slide 3: Pin configuration of 8085
8-bit general purpose μp
Capable of addressing 64 k of memory
Has 40 pins
Requires +5 v power supply
Can operate with 3 MHz clock

## Slide 4: Pin configuration of 8085
All the signals can be classified into
Six groups –
  Address Bus
  Data Bus
  Control & Status signals
  Power signal & frequency signals
  Externally initiated signals
  Serial I/O ports

## Slide 5: Address & data bus
8085 μp consists of 16 signal pins use as address bus.
Divide into 2 part: A15 – A8 (upper)
AD7 – AD0 (lower).
  A15 – A8 : Unidirectional, known as ‘high order address’.
  AD7 – AD0 : bidirectional and dual purpose (address and data placed
  once at a time).
  AD7 – AD0 also known as ‘low order address’.
  To execute an instruction, at early stage AD7 – AD0 uses as address bus and alternately as data bus for the next cycle.
  The method to change from address bus to data bus known as ‘bus multiplexing’.

## Slide 6: Control & Status signals
This group of signal includes-
    Two control signals (RD’ & WR’)
    Three status signals (IO/M’ , S1 & S0)
    One special signal (ALE)
RD’ – Read (active low). To indicate that the I/O or memory selected is to be read and data are available on the bus.
WR’ – Write (Active low). This is to indicate that the data available on the bus are to be written to memory or I/O ports.
IO/M’ – To differentiate I/O operation or memory operations.
      ‘0’ - indicates a memory operation.
      ‘1’-indicates an I/O operation.
      IO/M’ combined with RD and WR to generate I/O and memory control signals.

## Slide 7: Control and Status Signals.
  S1 and S0: Status signals, similar to IO/M, can identify various
  operations as shown on the following table :

## Slide 8: Control & Status signals
  ALE (Address Latch Enable) signal :
    ALE used to de-multiplex address/data bus
    Active high signal - generated to show the start of 8085 operation.
    When transition 1-to-0: indicate that lines AD7-AD0
    (AD7-AD0 = A7-A0) act as address lines.

## Slide 9: Power signal & frequency signals
Vcc : +5 V power supply
Vss : Ground reference
X1 & X2 : A crystal is connected at these two pins. The frequency is divided by two.
Therefore, to operate a system at 3 MHz, the crystal should have a frequency of 6 MHz.
CLK OUT : This signal is used as the system clock for other devices.

## Slide 10: Externally initiated Signals including Interrupt

## Slide 11: Externally initiated Signals including Interrupt
RESET IN’ : When the signal on this pin goes low,
  the program counter is set to zero.
  the buses are tri-sated.
  MPU is reset.
RESET OUT : This signal is used to reset other
devices.

## Slide 12: Serial I/O ports
The 8085 has two signals to implement the
serial transmission:
    SID: Serial Input Data
    SOD: Serial Output Data

## Slide 13: Limitations of 8085
The low order address bus is multiplexed with the data bus. The buses need to be de-multiplexed.
Appropriate control signals need to be generated to interface memory and I/O with the 8085.

## Slide 14: De-multiplexed Address & Data bus with Control Signals

## Slide 15: Internal Architecture of 8085
It includes-
  ALU
  Timing & Control Unit
  Instruction Register and Decoder
  Register Array
  Interrupt Control
  Serial I/O Control

## Slide 16: 8085Single board Microcomputer System

## Slide 17: Reference Book “Microprocessor Architecture, Programming and Applications with 8085”, 5thEdition, Prentice Hall by Ramesh S. Goankar

## Slide 18: END